## Slide 1
KOFORIDUA TECHNICAL UNIVERSITY
Faculty of Applied Science and Technology – Department of Computer Science
DESIGN AND SIMULATION OF AN IoT-BASED SMART ENERGY MONITORING NETWORK WITH ALERT SYSTEM
Project Defense Presentation
Presented by: Nuhu Abdulai (B202220513)
Supervisor: Dr. Bright Selorm Kodzo Anibrika
2025/2026

## Slide 2
1
Background of the Study
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
2
• Electrical energy is a fundamental driver of modern society – global electricity demand grew by 2.2% in 2023 and is still accelerating (IEA, 2024).
• In Ghana, residential electricity consumption accounts for about 40% of total national demand (Electricity Company of Ghana).
• Traditional analogue (electromechanical) meters only record cumulative monthly usage and require manual reading – no real-time insight into usage patterns, peak demand, or device-level consumption.
• The Internet of Things (IoT) enables smart meters and sensors to continuously measure voltage, current, power, and energy, transmitting data wirelessly for processing and visualisation (Gubbi et al., 2013).
• Real-time feedback on energy usage has been shown to reduce residential consumption by 5–15% (Faruqui et al., 2010).
• This project therefore proposes a simulation-based IoT smart energy monitoring and alert system for a residential building – built entirely with lightweight, accessible web technologies.

## Slide 3
2
Problem Statement
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
3
Most residential consumers lack effective tools to monitor energy in real time; conventional metering only provides cumulative data at the end of each billing cycle. This delayed feedback model causes:
• Lack of awareness
  – Consumers cannot see what different appliances consume, leading to unintentional waste.
• Delayed detection of faults
  – A malfunctioning appliance drawing excessive power may go unnoticed for weeks, raising both energy costs and fire risk.
• Peak demand blind spots
  – Without real-time data, users cannot identify peak usage periods or avoid high-tariff hours.
• No alert mechanism
  – Existing meters do not notify users when consumption exceeds thresholds – leaving them vulnerable to bill shock.
Gap addressed: a system that continuously measures, transmits, and visualises electrical parameters and proactively alerts users to abnormal conditions.

## Slide 4
3
Objectives of the Study
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
4
Main Objective (Aim): To design and simulate an IoT-based smart energy monitoring network with an alert system that provides real-time information about electricity consumption in a residential building.
• Specific Objective 1 – Design & Simulation: design a system architecture that simulates multiple smart meters, and develop a device simulator generating realistic electrical data (power, voltage, current, energy, temperature, humidity) for 20 virtual meters.
• Specific Objective 2 – Backend & Dashboard: implement a Flask-based backend that receives, stores, and broadcasts sensor data via REST API and WebSocket, and a real-time web dashboard with live charts, device cards, and a status map.
• Specific Objective 3 – Alerts & Validation: implement a threshold-based alert engine that detects abnormal readings and notifies users, and validate the system through unit, integration, and security testing.

## Slide 5
4
Literature Review
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
5
Four systems were reviewed; each analysed with the three process models – Use Case Diagram, Sequence Diagram, and ERD (structural).
System | Use Case Diagram | Sequence Diagram | ERD (Structural)
AWS IoT Core + Analytics | Devices publish to MQTT; cloud routes, stores & analyses; dashboards | Meter → MQTT → Rule → DynamoDB → Analytics → QuickSight | Device, Shadow, Rule, Reading
openHAB | Bindings integrate 200+ protocols; rules react to state changes | Sensor → binding → rule engine → alert (email / push) | Item, Binding, Rule, Persistence
Blynk | Device syncs to cloud; user builds widget dashboards (mobile) | ESP32 → Blynk cloud → mobile app (real time) | Device, Virtual Pin, Widget
ESP32 + PZEM-004T | Meter measures AC load; server stores & displays | ESP32 (Modbus) → PZEM → HTTP POST → server | Sensor, Reading, Server
• Network Simulation – 1 network architecture reviewed: AWS IoT Core network (smart meters ↔ MQTT broker ↔ rules engine ↔ DynamoDB ↔ IoT Analytics ↔ QuickSight).
• AI/ML – 1 system reviewed: AWS IoT Analytics, an ML-capable cloud analytics service for IoT data at scale.
• Research gap: existing solutions are too complex, too costly, or hardware-dependent – calling for a lightweight simulation-based alternative.

## Slide 6
5
Methodology
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
6
A. Software Development – 3 process models
• Process model: Agile (Scrum) – iterative, rapid feedback, documentation-light (Beck et al., 2001).
• Justified by incremental delivery, evolving requirements, early testing, and reduced risk.
• Use Case Diagram – actors (User, System) and 8 use cases.
• Sequence Diagram – simulator → API → database → alert engine → WebSocket → dashboard.
• ERD / Class Diagram – Device, Reading, Alert (one-to-many).
B. Network Simulation – physical and logical network diagrams
Physical Network Diagram (LAN)
Device Simulator
Backend (Flask + SQLite)
Dashboard (browser)
All components on a local network – no cloud subscription and no hardware wiring.
Logical Network Diagram (publish–subscribe)
Simulator
Backend + SQLite
Dashboards
HTTP POST: simulator publishes readings → backend validates, persists, runs alert engine → WebSocket broadcasts to all dashboards in real time.
C. AI/ML – architectural model and justification
Reading
Validate
Threshold check
Alert → notify + DB
• Justification: deterministic, transparent, configurable per device; no training data or hardware needed.
• ML anomaly detection identified as future work.

## Slide 7
6
Results and Analysis – Testing (1 of 2)
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
7
86
Test cases passed (149 assertions)
20
Virtual smart meters simulated
7
Abnormal conditions detected
3 s
Simulator → dashboard update
• Verification testing
  – Unit tests (auth, alert engine, API validation) + integration tests of the end-to-end pipeline – all passed.
• Validation testing
  – 6 scenarios passed: device simulation, real-time dashboard updates, threshold alerts, alert acknowledgement, offline detection, colour-coded device map.
• System security testing
  – Malformed JSON → HTTP 400 (no crash); XSS attempts escaped in rendered HTML; no credentials leaked in API responses.
• Alert engine coverage
  – Over-voltage (>250 V), under-voltage (<200 V), over-current (>30 A), high-power (>5000 W), high/low temperature (>50 °C / <10 °C), and device offline – correct severity levels.
• Outcome: no critical or high-severity issues; system ready for demonstration and deployment.

## Slide 8
6
Results and Analysis – Key Findings (2 of 2)
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
8
• Real-time monitoring is feasible with web technologies
  – Flask REST + Flask-SocketIO delivered readings to the dashboard within the same 3-second interval, with no measurable delay.
• Alert engine enhances awareness
  – Correctly detected all 7 anomaly types with appropriate severity levels (critical/warning).
• Data visualisation improves comprehension
  – Chart.js charts revealed peak usage hours and anomalous readings at a glance.
• Simulation is a valid educational approach
  – 20 virtual meters generated realistic residential patterns without hardware cost, wiring, or safety concerns.
• Proper authentication is critical
  – Moving from demo auto-login to password-verified authentication with bcrypt (werkzeug.security) closed a significant security gap.

## Slide 9
7
Conclusions and Recommendations
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
9
Conclusions
• All objectives achieved – 20 simulated meters, Flask backend (REST + WebSocket), SQLite storage, real-time dashboard, and alert engine.
• All 86 test cases passed, confirming functional, integration, and security requirements.
• IoT energy monitoring can be effectively implemented with lightweight, accessible web technologies – no physical hardware or cloud subscription required.
• Provides a foundation for future physical IoT deployments and an educational resource for energy management and IoT.
Recommendations for Future Work
• Hardware integration – replace simulator with ESP32 + PZEM-004T (API already accepts real data).
• Machine learning for anomaly detection beyond fixed thresholds.
• Mobile application (Flutter/React Native) with push notifications.
• Cloud deployment (AWS, Heroku, PythonAnywhere) for remote access.
• Historical analytics – daily/weekly/monthly reports, trends, cost estimation.
• Multi-building / campus-wide support.
• Smart-home voice integration (Google Home, Amazon Alexa, Apple HomeKit).

## Slide 10
8
References
Design and Simulation of an IoT-Based Smart Energy Monitoring Network with Alert System
10
• Al-Ali, A. R., Zualkernan, I. A., Rashid, M., et al. (2017). A smart home energy management system using IoT and big data analytics approach. IEEE Trans. Consumer Electronics, 63(4).
• Ashton, K. (2009). That ‘Internet of Things’ thing. RFID Journal, 22(7).
• Atzori, L., Iera, A., & Morabito, G. (2010). The Internet of Things: A survey. Computer Networks, 54(15).
• Beck, K., Beedle, M., van Bennekum, A., et al. (2001). Manifesto for Agile Software Development. Agile Alliance.
• Blynk Inc. (2024). Blynk IoT Platform Documentation. https://docs.blynk.io
• Faruqui, A., Sergici, S., & Sharif, A. (2010). The impact of informational feedback on energy consumption. Energy, 35(4).
• Gubbi, J., Buyya, R., Marusic, S., & Palaniswami, M. (2013). Internet of Things (IoT): A vision, architectural elements, and future directions. Future Generation Computer Systems, 29(7).
• International Energy Agency. (2024). Electricity Market Report 2024. IEA Publications.
• openHAB Foundation. (2024). openHAB Documentation. https://www.openhab.org/docs
• Statista. (2024). Internet of Things (IoT) market size worldwide. https://www.statista.com
• Zanella, A., Bui, N., Castellani, A., et al. (2014). Internet of Things for smart cities. IEEE Internet of Things Journal, 1(1).
• Flask Contributors. (2024). Flask Documentation (3.x). https://flask.palletsprojects.com